Hydra – Multi adapter for MSX

# About
Hydra is a multi controller adapter for MSX. It provides connection with wired controllers from several video games:

Nintendo
- NES
- SNES
- Nintendo 64
- Gamecube
- Wii Nunchuck
- SEGA
- Master System
- Genesis 3 button
- Genesis 6 button
- SONY
- Digital (PSONE)
- Dualshock
- Guitar

It also provides interface to a ps/2 mouse in three operation modes:
- Standard Mouse
- Mouse + Joystick emulation
- Joystick emulation

Additional features:
- Auto detection on startup
- OLED display for status
# Project Description
The circuit is built upon an ATMega328, a shift register, an OLED display and some cable adapters. The microcontroller runs a firmware developed upon Arduino environment using a bunch of third party libraries .

# BLOCK DIAGRAM
The circuit consists of an Arduino board with a CD4021 shift register.

Arduino
shift
register
select

SEGA
GENESIS
latch

clock

cmd

data

NES/
SNES
data

clock

latch

UP

DOWN

LEFT

RIGHT

B/A

C/START

clock

att

DUALSHOCK
/ GUITAR
data

ack

N64/
GAMECUBE
1 wire

UP

DOWN

LEFT

RIGHT

B/A

C/START

MSX
PULSE

NUNCHUCK
SDA

SCL

Display

SDA

SCL

Debug

Serial
INT0
PORT
B
EEPROM
64Kx8
SDA

SCL

# ARDUINO PIN USAGE
The circuit uses most of the pins of the Arduino yet the TXD line is kept free to add debug capacity.
Arduino/AVR	MSX	MOUSE	Display	WII	Dualshock	Genesis	NES/SNES	N64	Gamecube
0 / PD0								1wire
1 / PD1
2 / PD2	PULSE
3 / PD3					ATT	LATCH	LATCH
4 / PD4					CLOCK	CLOCK	CLOCK
5 / PD5					CMD	SELECT
6 / PD6					DATA
7 / PD7									1 wire
8 / PB0	UP
9 / PB1	DOWN
10 / PB2	LEFT
11 / PB3	RIGHT
12 / PB4	TRGA
13/ PB5	TRGB
(14)A0 / PC0						DATA
(15)A1 / PC1							DATA
(16)A2 / PC2		DAT
(17)A3 / PC3		CLK
(18)A4 / PC4			SCL	SCL
(19)A5 / PC5			SDA	SDA

# CONNECTOR PINOUT
## MSX Side – DE-9
DE-9	MSX	Direction
1	UP	OUT
2	DOWN	OUT
3	LEFT	OUT
4	RIGHT	OUT
5	+5V	POWER
6	TRG A	OUT
7	TRG B	OUT
8	PULSE	IN
9	GND	POWER

## Controllers Side DB-25

DB-25	Function	Direction
1	+5V
2
3
4
5
6
7
8
9
10
11
12
13	+3V3
14	GND
15
16
17
18
19
20
21
22
23
24
25	GND

# Buttons and controls Assignment
The buttons and digital controls have been mapped to MSX joystick buttons or button combinations. The analog controls have been mapped to equivalent directional controls but are available as paddles and are accessible through Basic
## Sega Master System (SMS)
SMS	MSX
UP	UP
DOWN	DOWN
LEFT	LEFT
RIGHT	RIGHT
BT1	TRG A
BT2	TRG B

## Sega Genesis 3 button
Sega 3B	MSX
UP	UP
DOWN	DOWN
LEFT	LEFT
RIGHT	RIGHT
A	TRG A
B	TRG B
C	TRG A+B
START	LEFT+RIGHT

## Sega Genesis 6 button
Sega 6B	MSX
UP	UP
DOWN	DOWN
LEFT	LEFT
RIGHT	RIGHT
A	TRG A
B	TRG B
C	TRG A+B
X	TRG A Autofire
Y	TRG B Autofire
Z	TRG A+B Autofire
START	LEFT+RIGHT
MODE	UP+DOWN

## NES
NES	MSX
UP	UP
DOWN	DOWN
LEFT	LEFT
RIGHT	RIGHT
A	TRG A
B	TRG B
START	LEFT+RIGHT
SELECT	UP+DOWN

## Super NES
SNES	MSX
UP	UP
DOWN	DOWN
LEFT	LEFT
RIGHT	RIGHT
A	TRG A
B	TRG B
X	TRG A Autofire
Y	TRG B Autofire
L	UP + LEFT
R	UP + RIGHT
START	LEFT+RIGHT
SELECT	UP+DOWN

## Nintendo 64
N64	MSX
D-UP	UP
D-DOWN	DOWN
D-LEFT	LEFT
D-RIGHT	RIGHT
A	TRG A
B	TRG B
Z	TRG A Autofire
L	UP + LEFT
R	UP + RIGHT
START	LEFT+RIGHT
C-UP	TRG A+UP
C-DOWN	TRG A+DOWN
C-LEFT	TRG A+LEFT
C-RIGHT	TRG A+RIGHT
X axis	PDL(5)[/6]
Y axis	PDL(1)[/2]
X Axis(*)	LEFT/RIGHT
Y Axis(*)	UP/DOWN

(*) Digital equivalent
## WII Nunchuck
N64	MSX
C	TRG A
Z	TRG B
X Axis(*)	LEFT/RIGHT
Y Axis(*)	UP/DOWN
X axis	PDL(5)[/6]
Y axis	PDL(1)[/2]
Accel X	PDL(7)[/8]
Accel Y	PDL(3)[/4]
Acell Z	PDL(9)[/10]

(*) Digital equivalent
## Gamecube
N64	MSX
D-UP	UP
D-DOWN	DOWN
D-LEFT	LEFT
D-RIGHT	RIGHT
A	TRG A
B	TRG B
X	TRG B Autofire
Y	UP+DOWN(*)
Z	TRG A Autofire
START	LEFT+RIGHT
L(**)	UP + LEFT
R(**)	UP + RIGHT
C-X axis(**)	TRG A + LEFT/RIGHT
C-Y axis(**)	TRG A + UP/DOWN
D-X axis(**)	LEFT/RIGHT
D-Y axis(**)	UP/DOWN
L	PDL(11)[/12]
R	PDL(9)[/10]
C-X axis	PDL(7)[/8
C-Y axis	PDL(3)[/4]
D-X axis	PDL(5)[/6]
D-Y axis	PDL(1)[/2]

(*) Y mapped as a SELECT button
(**) Digital equivalent

## Dualshock
Dualshock	MSX
D-UP	UP
D-DOWN	DOWN
D-LEFT	LEFT
D-RIGHT	RIGHT
Triangle	TRG A Autofire
Square	TRG B Autofire
Cross	TRG A
Ball	TRG B
L1	UP + LEFT
R1	UP + RIGHT
L2	DOWN+LEFT
R2	DOWN+RIGHT
START	LEFT+RIGHT
SELECT	UP+DOWN
L-X Axis (*)	LEFT/RIGHT
L-Y Axis(*)	UP/DOWN
R-X Axis (*)	TRG A + LEFT/RIGHT
R-Y Axis(*)	TRGA + UP/DOWN
L-X Axis	PDL(5)[/6]
L-Y Axis	PDL(1)[/2]
R-X Axis	PDL(7)[/4]
R-Y Axis	PDL(3)[/8]
L3	Not assigned
R3	Not assigned

(*) Digital equivalent

## Guitar Hero Controller
Guitar	MSX
GREEN_FRET	TRG A
RED_FRET	TRG B
YELLOW_FRET	RIGHT
BLUE_FRET	LEFT
ORANGE_FRET	DOWN
STAR_POWER	UP
STRUM (*)	PDL(1)[/2]
WHAMMY_BAR	PDL(3)[/4]
START(**)	PDL(5)[/6]
SELECT(***)	PDL(7)[/8]

(*) UP: 16 << IDLE << 32:DOWN
(**) PRESS:16<<IDLE
(***) PRESS:16<<IDLE

# Protocols
The paragraphs below give a brief explanation on the protocols used in the project
## NES/SNES
Both controllers use the same protocol and share the same pins. Detection is performed by the state of bit A. Two consecutive readings are performed to make the read function compatible with SNES.
If a NES controller is present and A button press it shall read 0x3F,0x3F.

SNES controller uses a similar protocol but uses 12 out of 16 bits, being the last 4 bits at HIGH level (otherwise it is a different controller). Button A is present at the 9th bit so a double 8 bit reading shall return 0xFF,0x3F;

sdafs
sdf

## Megadrive (Sega Genesis)
The Sega Genesis controller has some compatibility with ATARI controllers but even the regular 3 3 button controller have more buttons than wires available on DE-9 connector. To solve that problem the controller has one multiplexer that is commanded by one line (SELECT) coming from the console.

When that line is at HIGH level the controller shall read

And the other buttons are read with the line in LOW level.

The extra buttons on the 6 button controller are accessed by toggling the SELECT line three times in a row within a given interval

In Case of 3-Button-Controller

 Sel D0 D1 D2 D3 D4 D5
 Low UP DW LO LO A ST
 High UP DW LF RG B C

   # LO --- Always Low
   # UP --- Up of Cross Key
   # DW --- Down of Cross Key
   # LF --- Left of Cross Key
   # RG --- Right of Cross Key
   # A ---- Trigger Button A
   # B ---- Trigger Button B
   # C ---- Trigger Button C
   # ST --- Start Button
   ## Low -> Pressed , High -> Not Pressed

Data Aquisition Sequence of 6-Button-Controller

Sel D0 D1 D2 D3 D4 D5
Low UP DW LO LO A ST 0
High UP DW LF RG B C 1
Low UP DW LO LO A ST 2
High UP DW LF RG B C 3 # If there is two up-edge in 1.1 milli seconds,
Low LO LO LO LO A ST 4 # D0 - D3 go Low as Sel goes Low.
High Z Y X MD HI HI 5 # Make Sel High and read D0 - D3.
Low HI HI HI HI A ST 6 # Check that D0 - D3 go High as Sel goes Low.
High UP DW LF RG B C 7 # Once this sequence take place
Low UP DW LO LO A ST # sequence can't be started for 1.8 milli seconds
. # after the first up-edge of Sel.
. # Only Datas read in 1.6 milli seconds from the
. # first up-edge of Sel are reliable.

   # LO --- Always Low
   # HI --- Always High
   # UP --- Up of Cross Key
   # DW --- Down of Cross Key
   # LF --- Left of Cross Key
   # RG --- Right of Cross Key
   # A ---- Trigger Button A
   # B ---- Trigger Button B
   # C ---- Trigger Button C
   # X ---- Trigger Button X
   # Y ---- Trigger Button Y
   # Z ---- Trigger Button Z
   # ST --- Start Button
   # MD --- Mode Button
   ## Low -> Pressed , High -> Not Pressed

## Mouse
   // PS/2-mouse to MSX v1.1 //
  // Made By: NYYRIKKI 2014 //

The Mouse sketch was slightly modified. The detection shall occur at powerup or by pressing the RESET button.
LEFT – MOUSE mode
RIGHT – JOYSTICK mode
LEFT+RIGHT – Mouse plus emulated joystick

# Dualshock
Based on
https://github.com/madsci1016/Arduino-PS2X

* Super amazing PS2 controller Arduino Library v1.4
*	details and example sketch:
*	http://www.billporter.info/?p=240

# Gamecube
// Bit 7 6 5 4 3 2 1 0
//Byte 0 0 0 0 ST Y X B A
//Byte 1 1 L R Z Up Dw Rg Lf
//Byte 2 Joystick X Value (8 bit)
//Byte 3 Joystick Y Value (8 bit)
//Byte 4 C-Stick X Value (8 bit)
//Byte 5 C-Stick Y Value (8 bit)
//Byte 6 Left Button Value (8 bit) - may be 4-bit mode also?
//Byte 7 Right Button Value (8 bit) - may be 4-bit mode also?
a
# OLED Display
https://github.com/greiman/SSD1306Ascii